## Slide 1: Unit – 8 Instruction-Level Parallelism
dixita.kagathara@darshan.ac.in
+91 - 97277 47317 (CE Department)
Computer Engineering Department
Prof. Dixita B. Kagathara
Compiler Design (CD)
GTU # 3170701

## Slide 2

Looping
Topics to be covered
  Processor Architectures
  Code scheduling constrains
  Basic block Scheduling
  Pass structure of Assembler

## Slide 3: Processor Architecture

## Slide 4: Processor Architecture
When we think of instruction-level parallelism, we usually imagine a processor issuing several operations in a single clock cycle. In fact, it is possible for a machine to issue just one operation per clock and yet achieve instruction-level parallelism using the concept of pipelining.

## Slide 5: Instruction Pipelines and Branch Delays
Practically every processor, be it a high-performance supercomputer or a standard machine, uses an instruction pipeline. With an instruction pipeline, a new instruction can be fetched every clock while preceding instructions are still going through the pipeline.
Shown in below Fig. is a simple 5-stage instruction pipeline: it first fetches the instruction (IF), decodes it (ID), executes the operation (EX), accesses the memory (MEM), and writes back the result (WB).
The figure shows how instructions i, i + 1, i + 2, i + 3, and i + 4 can execute at the same time. Each row corresponds to a clock tick, and each column in the figure specifies the stage each instruction occupies at each clock tick.

## Slide 6: Instruction Pipelines and Branch Delays
If the result from an instruction is available by the time the succeeding instruction needs the data, the processor can issue an instruction every clock.
Branch instructions are especially problematic because until they are fetched, decoded and executed, the processor does not know which instruction will execute next. Many processors speculatively fetch and decode the immediately succeeding instructions in case a branch is not taken. When a branch is found to be taken, the instruction pipeline is emptied and the branch target is fetched.
Thus, taken branches introduce a delay in the fetch of the branch target and introduce "hiccups" in the instruction pipeline. Advanced processors use hard-ware to predict the outcomes of branches based on their execution history and to pre-fetch from the predicted target locations. Branch delays are nonetheless observed if branches are mis-predicted.

## Slide 7: Pipelined Execution
Some instructions take several clocks to execute.
One common example is the memory-load operation. Even when a memory access hits in the cache, it usually takes several clocks for the cache to return the data.
We say that the execution of an instruction is pipelined if succeeding instructions not dependent on the result are allowed to proceed.
Thus, even if a processor can issue only one operation per clock, several operations might be in their execution stages at the same time.
If the deepest execution pipeline has n stages, potentially n operations can be "in flight" at the same time.
Note that not all instructions are fully pipelined. While floating-point adds and multiplies often are fully pipelined, floating-point divides, being more complex and less frequently executed, often are not.
Most general-purpose processors dynamically detect dependences between consecutive instructions and automatically stall the execution of instructions if their operands are not available. Some processors, especially those embedded in hand-held devices, leave the dependence checking to the software in order to keep the hardware simple and power consumption low. In this case, the compiler is responsible for inserting "noop" instructions in the code if necessary to assure that the results are available when needed.

## Slide 8: Multiple Instruction Issue
By issuing several operations per clock, processors can keep even more operations in flight. The largest number of operations that can be executed simultaneously can be computed by multiplying the instruction issue width by the average number of stages in the execution pipeline.
Like pipelining, parallelism on multiple-issue machines can be managed either by software or hardware.
Machines that rely on software to manage their parallelism are known as VLIW (Very-Long-Instruction-Word) machines, while those that manage their parallelism with hardware are known as superscalar machines.
Simple hardware schedulers execute instructions in the order in which they are fetched.
If a scheduler comes across a dependent instruction, it and all instructions that follow must wait until the dependences are resolved (i.e., the needed results are available).
Such machines obviously can benefit from having a static scheduler that places independent operations next to each other in the order of execution.

## Slide 9: Multiple Instruction Issue
More sophisticated schedulers can execute instructions "out of order."
Operations are independently stalled and not allowed to execute until all the values they depend on have been produced.
Even these schedulers benefit from static scheduling, because hardware schedulers have only a limited space in which to buffer operations that must be stalled. Static scheduling can place independent operations close together to allow better hardware utilization.
More importantly, regardless how sophisticated a dynamic scheduler is, it cannot execute instructions it has not fetched. When the processor has to take an unexpected branch, it can only find parallelism among the newly fetched instructions.
The compiler can enhance the performance of the dynamic scheduler by ensuring that these newly fetched instructions can execute in parallel.

## Slide 10: Code-Scheduling Constraints

## Slide 11: Code-Scheduling Constraints
Code scheduling is a form of program optimization that applies to the machine code that is produced by code generator.
Code scheduling subject to three kinds of constraints:
  Control dependence constraints: All the operations executed in the original program must be executed in the optimized one.
  Data dependence constraints: The operations in the optimized program must produce the same result as the corresponding ones in the original program.
  Resource constraints: The schedule must not oversubscribe the resources one the machine.

## Slide 12: Code-Scheduling Constraints
These scheduling constraints guarantee that the optimized program produces the same result as the original.
However, because code scheduling changes the order in which the operation execute, the state of the memory at any one point may not match any of the memory states in a sequential execution.
This situation is a problem if a program’s execution is interrupted by, for example, a thrown exception or a user interested breakpoint.
Optimized programs are therefore harder to debug.

## Slide 13: Basic-Block Scheduling

## Slide 14: Basic-Block Scheduling
Data-Dependence Graphs
List Scheduling of Basic Blocks
Prioritized Topological Orders

## Slide 15: Data-Dependence Graphs
We represent each basic block of machine instructions by a data-dependence graph, G = (N,E), having a set of nodes N representing the operations in the machine instructions in the block and a set of directed edges E representing the data-dependence constraints among the operations. The nodes and edges of G are constructed as follows:
Each operation n in N has a resource-reservation table RTn, whose value is simply the resource-reservation table associated with the operation type of n.
Each edge e in E is labeled with delay de indicating that the destination node must be issued no earlier than de clocks after the source node is issued. Suppose operation n± is followed by operation n2, and the same location is accessed by both, with latencies l1 and l2 respectively. That is, the location's value is produced l1 clocks after the first instruction begins, and the value is needed by the second instruction l2 clocks after that instruction begins Then, there is an edge n1  n2 in E labeled with delay l1 — l2

## Slide 16: List Scheduling of Basic Blocks
The simplest approach to scheduling basic blocks involves visiting each node of the data-dependence graph in "prioritized topological order.
Since there can be no cycles in a data-dependence graph, there is always at least one topological order for the nodes. However, among the possible topological orders, some may be preferable to others.
There is some algorithm for picking a preferred order.

## Slide 17: Prioritized Topological Orders
List scheduling does not backtrack; it schedules each node once and only once. It uses a heuristic priority function to choose among the nodes that are ready to be scheduled next. Here are some observations about possible prioritized orderings of the nodes:
Without resource constraints, the shortest schedule is given by the critical path, the longest path through the data-dependence graph. A metric useful as a priority function is the height of the node, which is the length of a longest path in the graph originating from the node.
On the other hand, if all operations are independent, then the length of the schedule is constrained by the resources available. The critical resource is the one with the largest ratio of uses to the number of units of that resource available. Operations using more critical resources may be given higher priority.
Finally, we can use the source ordering to break ties between operations; the operation that shows up earlier in the source program should be scheduled first

## Slide 18: Pass structure of assembler

## Slide 19: Pass structure of assembler
A complete scan of the program is called pass.
Types of assembler are:
  Two pass assembler (Two pass translation)
  Single pass assembler (Single pass translation)

## Slide 20: Two pass assembler (Two pass translation)
l
Pass I
Pass II
Source Program
Target Program
Intermediate code
Control transfer
Data structures
Data access
l
l
l
l

## Slide 21: Two pass assembler (Two pass translation)
The first pass performs analysis of the source program.
The first pass performs Location Counter processing and records the addresses of symbols in the symbol table.
It constructs intermediate representation of the source program.
Intermediate representation consists of following two components:
  Intermediate code
  Data structures
Pass I
Pass II
Source Program
Target Program
Intermediate representation
Intermediate code
Data structures

## Slide 22: Two pass assembler (Two pass translation)
The second pass synthesizes the target program by using address information recorded in the symbol table.
Two pass translation handles a forward reference to a symbol naturally because the address of each symbol would be known before program synthesis begins.
Pass I
Pass II
Source Program
Target Program
Intermediate representation
Intermediate code
Data structures
Use of a Symbol that precedes its definition in a program.

## Slide 23: One pass assembler (One pass translation)
A one pass assembler requires one scan of the source program to generate machine code.
Location counter processing, symbol table construction and target code generation proceed in single pass.
The issue of forward references can be solved using a process called back patching.

## Slide 24: References
Books:
Compilers Principles, Techniques and Tools, PEARSON Education (Second Edition)
Authors: Alfred V. Aho, Monica S. Lam, Ravi Sethi, Jeffrey D. Ullman
Compiler Design, PEARSON (for Gujarat Technological University)
Authors: Alfred V. Aho, Ravi Sethi, Jeffrey D. Ullman

## Slide 25: Thank You